We can capture how the errors we are interested in change over time by deriving our kinematic model around these errors as our new state vector.
The new state is [x,y,ψ,v,cte,eψ].
Let’s assume the vehicle is traveling down a straight road and the longitudinal direction is the same as the x-axis.
### Cross Track Error
Then we can express the error between the center of the road and the vehicle's position as the cross track error:
cte​t+1​​=cte​t​​+v​t​​∗sin(eψ​t​​)∗dt
In this case cte​t​​ can be expressed as the difference between the line and the current vehicle position y. Assuming the reference line is a 1st order polynomial f:
cte​t​​=f(x​t​​)−y​t​​
If we substitute cte​t​​ back into the original equation the result is:
cte​t+1​​=f(x​t​​)−y​t​​+(v​t​​∗sin(eψ​t​​)∗dt)
This can be broken up into two parts:
1. f(x​t​​)−y​t​​ being current cross track error.
2. v​t​​∗sin(eψ​t​​)∗dt being the change in error caused by the vehicle's movement.
### Orientation Error
Ok, now let’s take a look at the orientation error:
eψ​t+1​​=eψ​t​​+​L​f​​​​v​t​​​​∗δ​t​​∗dt
The update rule is essentially the same as ψ.
eψ​t​​ is the desired orientation subtracted from the current orientation:
eψ​t​​=ψ​t​​−ψdes​t​​
We already know ψ​t​​, because it’s part of our state. We don’t yet know ψdes​t​​ (desired psi) - all we have so far is a polynomial to follow. ψdes​t​​ can be calculated as the tangential angle of the polynomial f evaluated at x​t​​, arctan(f​′​​(x​t​​)).f​′​​ is the derivative of the polynomial.
eψ​t+1​​=ψ​t​​−ψdes​t​​+(​L​f​​​​v​t​​​​∗δ​t​​∗dt)
Similarly to the cross track error this can be interpreted as two parts:
1. ψ​t​​−ψdes​t​​ being current orientation error.
2. ​L​f​​​​v​t​​​​∗δ​t​​∗dt being the change in error caused by the vehicle's movement.